## Slide 1
ECE 385 – Digital Systems Laboratory
Lecture 6 – Lab 6: CPU Design
Chushan Li
FALL 2021
Link to Course Website
Notes: ECE Main Slide

## Slide 2
About ECE 385 & Lab 6
ECE 385 Digital Systems Laboratory is a lab course, but not a lab-only course
In each week,
2 hours lecture: basic concept in digital system design
+ around 9 hours after class programming
+ 3 hours in Lab testing and demo
Lab1-3: TTL circuit based design, to get familiar with digital system and traditional design method
Lab4-5: Adder and Multiplier design: to learn the circuit module design in FPGA, using SystemVerilog
Lab6: LC3 CPU design: to learn how to construct basic CPU in FPGA
Lab7: System with Nois II Core: SoC design introduction
Lab8-9: USB keyboard, VGA display and customized modules: interface with outside equipment
Final Project: Game Controller, 3D Processor, whatever you want to design

## Slide 3
SLC-3 Block Diagram
Combinational Logic Circuit
Sequential Logic Circuit
Your key task:
Program the state machine in control block, realize the whole instructions set!
Where is the data flow?
How to control the datapath?
Notes: Note, big bold line is the 16-bit CPU bus. There is only a single bus, MUXes and load-enables control at every cycle what gets loaded

## Slide 4
Before the control design, how to interpret these instructions?
Let take ADD R2, R1, R0 @0x3000 as an example to show the data flow and the control of all bits!
SLC-3 ISA – Subset of LC-3 ISA
ADD R2, R1, R0 @0x3000
ADD: 0001
DR: R2 (010)
SR1: R1 (001)
SR2： R0 (000)
IR Address: 0x3000
0001 010 001 000 000 @0x3000
Notes: Note: NZP appears twice. Lower case nzp is value of register, upper case NZP is value from IR

## Slide 5
Partial State Diagram
State 18: Fetch_1
  Current State: PC=0x3000
  LD.MAR=1
  LD.PC=1
  PCMUX=10 (PC++);
  GatePC=1;
After State 18: Fetch_1
  PC=0x3001
  MAR=0x3000
Notes: For week 1, focus on first 3 states
Week 2 will have you make the rest of the states
Note how we wait for R, R is ready signal from memory
In practice, SRAM is fast compared to our 50MHz clock, so just wait extra cycle for read

## Slide 6
Partial State Diagram
State 33: Fetch_2
  Current State: MAR=0x3000
  LD.MDR=1
  MIO.EN=1
  CE, OE=1
After State 33: Fetch_2
  MDR=0001 010 001 000 000 (ADD R2, R1, R0 )
Notes: For week 1, focus on first 3 states
Week 2 will have you make the rest of the states
Note how we wait for R, R is ready signal from memory
In practice, SRAM is fast compared to our 50MHz clock, so just wait extra cycle for read

## Slide 7
Partial State Diagram
State 35: Fetch_3
  Current State: MDR=0001 010 001 000 000
  GateMDR=1
  LD.IR=1
After State 35: Fetch_3
  IR=0001 010 001 000 000 (ADD R2, R1, R0 )
Notes: For week 1, focus on first 3 states
Week 2 will have you make the rest of the states
Note how we wait for R, R is ready signal from memory
In practice, SRAM is fast compared to our 50MHz clock, so just wait extra cycle for read

## Slide 8
Partial State Diagram
State 32: Decode
  Current State: IR=0001 010 001 000 000
  Case (IR[15:12])
    0001: NextState= 1 (ADD)
  LD.BEN=1
After State 32: Decode
  BEN is loaded, but not used here because next operation is ADD
Notes: For week 1, focus on first 3 states
Week 2 will have you make the rest of the states
Note how we wait for R, R is ready signal from memory
In practice, SRAM is fast compared to our 50MHz clock, so just wait extra cycle for read

## Slide 9
Partial State Diagram
State 1: ADD(Execution)
  Current State: IR=0001 010 001 000 000
  DRMux=0 (IR[11:9], R2:010)
  SR2Mux=0 (SR2 Reg)
  SR1Mux=0 (IR[8:6], R1:001)
After State 1: ADD(Execution)
  NZP Reg is loaded, DR is loaded
  SR2: IR[2:0], R0:000
  ALUKMux=0 (ADD)
  GateALU=1
  LD.REG=1, LD.CC=1
Notes: For week 1, focus on first 3 states
Week 2 will have you make the rest of the states
Note how we wait for R, R is ready signal from memory
In practice, SRAM is fast compared to our 50MHz clock, so just wait extra cycle for read

## Slide 10
Understanding the data flow and control bits setting for all Instruction Cycle
My advice:
  Print out ~10 copies of SLC block diagram
  With different colored highlighter, trace out direction each MUX goes for each clock cycle in FETCH, DECODE and EXECUTE
  FETCH should be common for all instructions
  DECODE & EXECUTE will be different depending on instruction, start with a blank copy of block diagram and decide the DECODE & EXECUTE cycles for each instruction